## Slide 1
SSD Firmware
Architecture
FE
FTL
BE
A real NVMe SSD — controller, DRAM & NAND

## Slide 2
ROADMAP
Contents — 13 Sections
02 / 32
SSD Firmware Architecture
01
Why Firmware Exists
02
Controller Hardware
03
Three-Layer Model
04
Front-End (FE)
05
Flash Translation Layer
06
Back-End (BE)
07
DRAM Management
08
Multi-Core Firmware
09
Boot Sequence
10
Firmware Update
11
Power-Loss Recovery
12
QoS & Scheduling
13
End-to-End Write Path

## Slide 3
SECTION 1 · FOUNDATIONS
Why Firmware Exists: NAND's 3 Problems
03 / 32
SSD Firmware Architecture
No in-place update
▸ A page can't be overwritten — the whole block must be erased first, then reprogrammed.
#1
Asymmetric granularity
▸ Read/write act on pages (~16 KB); erase acts on blocks (many MB).
#2
Limited endurance
▸ Each block survives a finite number of Program/Erase (P/E) cycles.
#3
The fix: a log-structured design
Write new data to free pages sequentially; mark the old copy stale; a mapping table tracks each LBA's current location; garbage collection reclaims stale space later.
REAL-WORLD: A raw NAND USB stick with no FTL would wear out its first blocks in days — firmware is what makes flash last years.

## Slide 4
SECTION 1 · FOUNDATIONS
The Three Pillars of SSD Firmware
04 / 32
SSD Firmware Architecture
FTL
Address Translation
▸ Maintain the Logical→Physical (L2P) mapping so any LBA is found instantly.
GC
Garbage Collection
▸ Reclaim space from blocks full of stale pages by relocating valid data & erasing.
WL
Wear Leveling
▸ Spread P/E cycles evenly so all blocks wear out at roughly the same rate.
REAL-WORLD: Production SSD firmware is 500K–2M+ lines of C/C++ on multi-core ARM/RISC-V with hard real-time constraints.

## Slide 5
SECTION 2 · HARDWARE
Controller Hardware at a Glance
05 / 32
SSD Firmware Architecture
CONTROLLER SoC
Host Interface
PCIe/NVMe PHY • Gen4 x4 • DMA
CPU SUBSYSTEM
Core 0
Core 1
Core 2
Core 3
SRAM
512KB–2MB
ECC
LDPC/BCH
DRAM Controller
256MB–4GB
Flash Controller
8 channels • timing • DMA
8× NAND
channels
The real thing
REAL-WORLD: A Gen4 controller (Phison E18, Samsung Elpis) packs 5–8 cores and 8 NAND channels to reach ~7 GB/s.

## Slide 6
SECTION 2 · HARDWARE
What Each Block Does
06 / 32
SSD Firmware Architecture
Block
Function
PCIe/NVMe PHY
Physical link to host (Gen3/4/5, x4 lanes)
NVMe Accelerator
HW-assisted SQ/CQ management & command parsing
CPU Subsystem
2–8 ARM Cortex-R / RISC-V cores; runs firmware
SRAM
On-chip fast memory for FW code, stack, critical data
DRAM Controller
External DRAM for L2P table, write buffer, read cache
ECC Engine
Hardware LDPC/BCH encoder + decoder
Flash Controller
Per-channel NAND control, DMA, timing generation
Crypto Engine
HW AES-256 XTS for self-encrypting drive (SED)
Rule of thumb
≈ 1 GB DRAM per 1 TB of NAND — for a full page-level L2P mapping table.

## Slide 7
SECTION 3 · ARCHITECTURE
The Three-Layer Firmware Model
07 / 32
SSD Firmware Architecture
HOST (NVMe driver)
PCIe / NVMe
FRONT-END (FE)
NVMe cmd processing • SQ/CQ • PRP/SGL DMA • interrupts • namespaces
ftl_read / ftl_write / ftl_trim / ftl_flush
FLASH TRANSLATION LAYER (FTL)
L2P mapping • GC • wear leveling • bad-block mgmt • TRIM • power-loss recovery
be_nand_read / program / erase / status
BACK-END (BE)
NAND channel control • ECC • read retry • multi-plane/die scheduling • suspend/resume
NAND interface
NAND FLASH DIES
Each layer one job, one clean interface

## Slide 8
SECTION 3 · ARCHITECTURE
Interface Contracts Between Layers
08 / 32
SSD Firmware Architecture
FE → FTL
ftl_read(lba, len, buf)
ftl_write(lba, len, buf)
ftl_trim(lba, len)
ftl_flush()
FTL → BE
be_nand_read(ch, die, blk, pg, buf)
be_nand_program(ch, die, blk, pg, buf)
be_nand_erase(ch, die, blk)
be_nand_status(ch, die) → ready/busy
REAL-WORLD: Clean interfaces let each layer be tested independently and mapped to different CPU cores.

## Slide 9
04
Front-End (FE)
Speaking the host's language: NVMe command processing
09 / 32
SSD Firmware Architecture

## Slide 10
SECTION 4 · FRONT-END
4.1 NVMe Command Pipeline
10 / 32
SSD Firmware Architecture
HOST
SSD CONTROLLER (FE → FTL)
1 Write SQE
cmd → Submission Queue
2 Ring Doorbell
SQ Tail Doorbell reg
3 Fetch SQE
DMA read, 64 B
4 Parse + Validate
opcode, LBA, NLB, PRP
5 Dispatch to FTL
internal request
On completion
Build CQE → DMA to CQ → MSI-X IRQ → host
REAL-WORLD: On an NVMe gaming SSD at QD32, dozens of these flows run in parallel across queue pairs, each MSI-X vector pinned to a core.

## Slide 11
SECTION 4 · FRONT-END
4.2 Submission / Completion Queues
11 / 32
SSD Firmware Architecture
How SQ/CQ work
▸ Pointers: SSD tracks head/tail per SQ and CQ
▸ SQ Doorbell: host write signals new commands are ready
▸ Fetch: FE DMA-fetches 64-byte SQ entries
▸ Post: FE DMA-writes 16-byte CQ entries back
▸ Phase Tag (P): flips so host detects new completions
QUEUE PAIR
Submission Q
host → SSD (64 B)
Completion Q
SSD → host (16 B)
Up to 64K queue pairs per the NVMe spec — one per CPU core for scaling.
REAL-WORLD: Per-core queue pairs are why NVMe scales to millions of IOPS where old AHCI/SATA had a single 32-deep queue.

## Slide 12
SECTION 4 · FRONT-END
4.3 Data Pointers: PRP vs SGL
12 / 32
SSD Firmware Architecture
PRP — Physical Region Page
▸ Two entries: PRP1 + PRP2 in the command
▸ Large transfers: PRP2 → a PRP List the FE walks
▸ Constraint: page-aligned segments
▸ Use: standard NVMe I/O
SGL — Scatter-Gather List
▸ Descriptors: Data Block / Segment / Last Segment
▸ Flexible: arbitrary byte-aligned segments
▸ Use: NVMe-oF & advanced hosts
PRP LIST WALK
PRP1: 0x1000
page 1
PRP2 → List
@ 0x5000
0x3000
page 2
0x7000
page 3
0x9000
page 4
0xB000
page 5
REAL-WORLD: NVMe-over-Fabrics relies on SGLs because RDMA transfers rarely land on neat 4 KB page boundaries.

## Slide 13
SECTION 4 · FRONT-END
4.4 Interrupts: Pin → MSI → MSI-X
13 / 32
SSD Firmware Architecture
Scheme
Vectors
How it works
Pin-based
1
Sets a shared line / pending bit (legacy)
MSI
up to 32
Controller writes to a host memory address
MSI-X
up to 2048
Per-CQ vector + address/data pair
Why MSI-X matters
Each Completion Queue gets its own vector, so completions steer to a specific CPU core — keeping cache-hot data local (NUMA locality).
REAL-WORLD: A 64-core database server maps one CQ + MSI-X vector per core, so each core handles only its own I/O.

## Slide 14
05
Flash Translation Layer
The heart of the firmware: mapping, GC, wear, TRIM
14 / 32
SSD Firmware Architecture

## Slide 15
SECTION 5 · FTL
5.1 L2P Mapping Table
15 / 32
SSD Firmware Architecture
L2P TABLE (LPN → physical address)
LPN 0
→ ch0 die0 blk100 pg5
LPN 1
→ ch2 die1 blk200 pg12
LPN 2
→ UNMAPPED (trimmed)
LPN 3
→ ch1 die0 blk050 pg3
PPA packed into 4 bytes
▸ [31:28] Channel (16)
▸ [27:26] Die (4)
▸ [25] Plane (2)
▸ [24:11] Block (16K)
▸ [10:0] Page (2K)
REAL-WORLD: Every host write updates one L2P entry — this table is the single most accessed structure in the firmware.

## Slide 16
SECTION 5 · FTL
5.1 DRAM Sizing & DRAM-less (HMB)
16 / 32
SSD Firmware Architecture
Capacity
Entries
L2P DRAM
256 GB
64 M
256 MB
1 TB
256 M
1 GB
2 TB
512 M
2 GB
Rule of thumb
≈ 1 GB DRAM per 1 TB NAND (4 KB LBAs, 4-byte entries)
DRAM-less options (HMB)
▸ HMB: borrow 32–64 MB of host DRAM for warm L2P entries
▸ On-SRAM cache: small hot L2P cache in controller SRAM
▸ NAND-backed: full table in NAND, paged in on miss (adds latency)
REAL-WORLD: The Steam Deck's M.2 2230 SSD is DRAM-less and leans on HMB to keep cost, size, and power down.

## Slide 17
SECTION 5 · FTL
5.2 Garbage Collection
17 / 32
SSD Firmware Architecture
VICTIM BLOCK
V
I
V
I
I
V
I
V
V = valid I = invalid (stale)
1 Read valid
pages 0,2,5,7
2 Write to fresh
new dest block
3 Update L2P
remap moved pages
4 Erase victim
→ free pool
Write Amplification (WAF)
WAF = NAND writes ÷ host writes. Ideal 1.0; sequential ≈1.0; random ≥3.0; low OP can spiral to 10×.
Victim selection
Greedy (most invalid) • Cost-Benefit (age × invalidity) • d-Choices (sample d, pick best).
REAL-WORLD: A random-write OLTP database can push WAF to 4–5×, so enterprise drives add 28% over-provisioning.

## Slide 18
SECTION 5 · FTL
5.3 Wear Leveling
18 / 32
SSD Firmware Architecture
Two flavors
▸ Dynamic: GC returns erased blocks to the pool; writes go to least-worn
▸ Static: proactively move cold data off low-wear blocks so they can be reused too
P/E CYCLES ACROSS BLOCKS
Without WL
With WL
uneven → early failure even → max lifetime
Goal
Every block reaches end-of-life at roughly the same time — no weak block fails early.
REAL-WORLD: Without static WL, rarely-touched OS files would 'pin' fresh blocks while hot logs burn out a few in months.

## Slide 19
SECTION 5 · FTL
5.4 Bad-Block Management (BBM)
19 / 32
SSD Firmware Architecture
Factory bad blocks
marked at manufacture, stored in the Bad Block Table (BBT)
Grown bad blocks
fail erase/program at runtime, or hit uncorrectable ECC on read
Handling
relocate valid data, map out the block, update the BBT in reserved NAND
REAL-WORLD: NAND ships with some factory-bad blocks from day one — the BBT is built during the very first firmware boot.

## Slide 20
SECTION 5 · FTL
5.5–5.6 TRIM & Over-Provisioning
20 / 32
SSD Firmware Architecture
TRIM / UNMAP FLOW
Host deletes file
FS issues TRIM
FTL marks UNMAPPED
L2P cleared
Pages → INVALID
GC skips copying
Read returns zeros
no NAND access
Over-Provisioning (OP)
Spare NAND beyond the advertised capacity (7% consumer, up to 28% enterprise). More OP → fewer valid-page copies per reclaimed block → lower WAF and steadier performance.
CAPACITY SPLIT
User capacity
OP
More OP shrinks user space but boosts endurance & QoS.
REAL-WORLD: Enabling TRIM (Windows & Linux do it automatically) is the biggest 'free' way to keep an SSD fast over time.

## Slide 21
06
Back-End (BE)
Talking to the silicon: parallelism, ECC, retries
21 / 32
SSD Firmware Architecture

## Slide 22
SECTION 6 · BACK-END
6.1 Four Levels of NAND Parallelism
22 / 32
SSD Firmware Architecture
Channel
independent buses
N× bandwidth
Die
interleave on a channel
hide tPROG/tBERS
Plane
multi-plane op per die
~2× per die
Page
multi-page read
~2× read BW
OVERLAPPED SCHEDULING (2 channels)
CH0
PROG
READ
wait
CH1
READ
ERASE
wait
REAL-WORLD: A 'super-block' spanning every channel/die/plane is the write unit that streams one big write at full speed.

## Slide 23
SECTION 6 · BACK-END
6.2 ECC (LDPC) Pipeline
23 / 32
SSD Firmware Architecture
WRITE (encode): Data 4 KB → LDPC Encoder (HW) → Data + Parity → NAND program
READ (decode): NAND → Raw + Parity → LDPC Decoder (HW) → Corrected data (5–50 iterations)
Decode type
Input
Strength
Latency
Hard-decision
binary 0/1
~40–60 bits/KB
~1 µs
Soft-decision
multi-level Vref (LLR)
100+ bits/KB
~10–50 µs
REAL-WORLD: SLC→BCH; MLC→BCH/LDPC; TLC→LDPC mandatory; QLC→strong multi-iteration LDPC. Denser flash needs stronger ECC.

## Slide 24
SECTION 6 · BACK-END
6.3 Read Retry — Escalation
24 / 32
SSD Firmware Architecture
NAND read → LDPC hard-decision decode
~1 µs • corrects ~40–60 bits/KB
decode fails ↓
Read Retry: shift Vref ±Δ, re-decode
up to 20–50 voltage-offset levels
decode fails ↓
Soft-Decision LDPC
multiple reads → LLR reliability • ~10–50 µs
decode fails ↓
UECC — uncorrectable
report to host / RAID recovery
Why decode fails
▸ Retention: cells slowly lose charge
▸ P/E wear: Vth distributions shift
▸ Read disturb: neighboring reads
▸ Temperature: shifts thresholds
REAL-WORLD: As a QLC drive ages, more reads fall through to soft-decision decoding — the hidden cause of read-latency creep.

## Slide 25
SECTION 6 · BACK-END
6.4 Program Suspend / Resume
25 / 32
SSD Firmware Architecture
WITHOUT suspend — read waits for the whole program
PROGRAM ~1.5 ms
READ waits → ~2 ms
WITH suspend/resume — read jumps the queue
PROG
SUSP
READ 75µs
RES
PROG cont.
The trade-off
tSUS+tRES ≈ 10–20 µs overhead; excessive suspends add 10–20% to tPROG — but read tail latency drops from ~2 ms to ~100 µs.
REAL-WORLD: This is what keeps a game load or app launch snappy even while the SSD flushes a big background write.

## Slide 26
SECTION 7 · SYSTEM
DRAM Management (1 GB on a 1 TB SSD)
26 / 32
SSD Firmware Architecture
L2P Mapping Table
~512 MB • 50%
Write Buffer
~256 MB • 25%
Read Cache
~128 MB • 12.5%
GC Buffer
~64 MB • 6.25%
FW Heap / Metadata
~64 MB • 6.25%
What each is for
▸ Mapping cache: hot L2P in DRAM, cold paged from NAND
▸ Write buffer: coalesce small writes, program full pages
▸ Read cache: exploit temporal locality
▸ PLP-protected: buffers survive power loss
REAL-WORLD: This split is why a 1 TB DRAM SSD ships with ~1 GB DRAM — most of it is just the mapping table.

## Slide 27
SECTION 8 · SYSTEM
Multi-Core Firmware Partitioning
27 / 32
SSD Firmware Architecture
Core 0
FE
▸ NVMe cmd • SQ/CQ • host DMA • admin
Core 1
FTL
▸ L2P • GC • WL • TRIM • journal
Core 2
BE
▸ channels 0–3 • ECC • retry
Core 3
BE / Mgmt
▸ channels 4–7 • SMART • thermal
SHARED DRAM / SRAM — L2P • buffers • lock-free ring buffers • HW mailboxes & semaphores
Critical section
The L2P table is touched by host read, host write, GC, and TRIM — guarded by per-LBA-range locks or partitioned per core.
REAL-WORLD: Real-time Cortex-R cores run latency-critical FE/BE; application cores handle GC and housekeeping.

## Slide 28
SECTION 9 · SYSTEM
Firmware Boot Sequence
28 / 32
SSD Firmware Architecture
1 Boot ROM
immutable • init clocks/SRAM • load + verify bootloader
2 Bootloader
train DRAM • detect NAND geometry • load + verify main FW
3 Main FW init
scan BBT • load L2P checkpoint / replay journal • init FE, GC, WL
4 Ready
set CSTS.RDY = 1 • start background tasks
Phase
Time
Boot ROM
1–10 ms
Bootloader+DRAM
50–200 ms
FW load+verify
20–500 ms
L2P rebuild
0.1–2 s
Total
~0.3–3 s
REAL-WORLD: Secure boot verifies each stage's RSA/ECDSA signature — why you can't flash arbitrary firmware onto a modern SSD.

## Slide 29
SECTION 10 · SYSTEM
Firmware Update: Dual-Bank (A/B)
29 / 32
SSD Firmware Architecture
Bank A — ACTIVE
v1.2 (running now)
Bank B — STANDBY
v1.1 (backup)
▸ 1 Download new FW → Bank B (NVMe FW Download 0x11)
▸ 2 Verify CRC / RSA signature
▸ 3 Firmware Commit (0x10) → set boot pointer to Bank B
▸ 4 Reset → boot from Bank B; Bank A becomes backup
▸ 5 If Bank B fails to boot → ROM falls back to Bank A
Why A/B?
▸ Safety: a bad image never bricks the drive
▸ Rollback: previous image always survives
REAL-WORLD: A single-bank budget SSD can brick if power drops mid-update — A/B is why fleets update safely under live I/O.

## Slide 30
SECTION 11 · SYSTEM
Power-Loss Recovery (SPOR)
30 / 32
SSD Firmware Architecture
NORMAL OPERATION
Every write
append journal {LPN, old→new PPA, seqno, CRC}
Every N writes / T sec
checkpoint dirty L2P pages to reserved NAND
RECOVERY ON NEXT BOOT
1 Load last L2P checkpoint
2 Replay journal after checkpoint
3 Scan open blocks for partial writes
4 Discard corrupted pages → consistent L2P
5 Resume
PLP hardware
Enterprise drives carry supercaps (~10–50 ms) to flush write buffer, dirty L2P & journal to NAND on power dip.
Golden rule
Update L2P only AFTER NAND program success — else a crash leaves a mapping to an unprogrammed page.
REAL-WORLD: Client SSDs often skip supercaps and accept losing only the last few unacknowledged writes.

## Slide 31
SECTION 12 · SYSTEM
QoS & Command Scheduling
31 / 32
SSD Firmware Architecture
WITHOUT QoS
read blocked by GC writes → ~10+ ms
WITH QoS (interleaved)
R
GC
R
GC
R
GC
→ ~100–200 µs
Techniques
▸ Watermarks: background GC early; urgent GC when low; never hit zero
▸ Rate-adaptive GC: aggressive when idle, minimal when busy
▸ Suspend/resume + priority + VWC/FUA: host I/O beats background
Percentile
Target
p50
~100 µs
p99
< 500 µs
p99.9
< 1 ms
p99.99
< 5 ms
REAL-WORLD: VWC acknowledges a write from DRAM (~10 µs); FUA=1 forces it to NAND first (DB commits, FS journals).

## Slide 32
SECTION 13 · END-TO-END
The Complete Host-Write Path (4 KB → NAND)
32 / 32
SSD Firmware Architecture
HOST
FE
FTL
BE
1 SQE + doorbell
2 fetch + parse
3 DMA data → write buffer
4 allocate free page (PPA)
5 update L2P + invalidate old
6 LDPC encode
7 PROGRAM 80h..10h
8 wait tPROG ~1.5 ms
9 journal entry (SPOR)
10 CQE + MSI-X → host
With Volatile Write Cache (FUA=0)
the command completes at step 3 — data safe in PLP-protected DRAM — and the NAND program happens in the background.